## Slide 1
AE668 : Computation Aeromechanics and Control of UAV
By :
Dharshan S Hegde
M.Tech UAS - 241010078
dharshans24@iitk.ac.in
Individual Project Presentation

## Slide 2
Design of tricopter for detection of cracks in high rise structures

## Slide 3
  Introduction
Table of Contents
  Performance and Weight Estimation
  Structural Analysis
  Control Aspect of Tricopter
  Conclusion

## Slide 4
Introduction
Objectives :
  Design a tricopter having an endurance of 30 min and can lift 200 grams of payload
  Describing the preliminary design process for building of a tricopter for the required payload like performance , control and structural parts.
  Different trajectory maneuvers and its response for the designed tricopter.
  Buildings or high bridges usually develop cracks due to its inability to withstand stress in the components over a period of time or due to natural calamities such as earthquakes.
  Detecting cracks during the early stage helps in longing the lifespan of the building and avoid catastrophic collapses. Detecting cracks is done as visual inspection by inspectors, which are usually time consuming, erroneous, dangerous and expensive.
  In order to monitor all the elements of the high raised buildings, ensure the safety of the inspector and to revise the crack images in various angles, drones can be used.
Source : POSCO

## Slide 5
CAD Design
Controller
Servo
Frame
Support Rod
Motor
Propeller
Camera & Gimbal
Current Design :
  Configuration : Tricopter
  Shape : Y Shaped (120 degrees apart)
  Arm Length : 250 mm
  Servo Control for yaw motion

## Slide 6
Performance & Weight Estimation

## Slide 7
Performance Estimation
  The hover performance of the tricopter is determined using Blade Element Momentum Theory .
  Using BEMT we obtain different parameters of performance which includes C_T (Thrust Coefficient) , C_Q (Torque Coefficient) & Figure of Merit .
Parameters considered :
  Rotor Radius - (0.1 m to 0.2 m)
  Number of blade in each rotor - 2
  Endurance - 30 min
  Payload Weight = 200 grams
  RPM Variation - 3000 to 7000

## Slide 8
Weight Estimation
Source : Winslow, J., Hrishikeshavan, V., & Chopra, I. (2018). Design methodology for small-scale unmanned quadrotors. Journal of Aircraft, 55(3), 1062–1070. https://doi.org/10.2514/1.C034483​
Inputs :
  R - Total radius [m]
  R_cut - Cut-off radius [m]
  sgm - Rotor solidity
  Nb - Number of blades
  C - Battery capacity [mAh]
  S - Number of cells
  I - Max req. current for motors [A]
  P - Max rated output power [Watts]
  Kv - Motor speed constant [Rev Per Min Per Volt]
  Imax - Max sustainable current through ESC [A]
Outputs:
  mR - Rotor mass [g]
  mB - Battery mass [g]
  mBL - BLDC motor mass [g]
  mEBL - ESC mass for BLDC motors [g]
  mA - Airframe mass [g]

## Slide 9
BEMT Parameters | BEMT Parameters
Number of blades in each rotor | 2
Number of rotors | 3
Battery | 4S
Rotor radius | 0.12 m
Total Thrust | 7.3
RPM | 5300
Hover Power | 29 W
Endurance | 30 min
Gross Weight | 730 grams
Figure of merit | 0.846
Thrust Coefficient | 2.654 * 10^-3
Torque Coefficient | 1.142 * 10^-4

## Slide 10
Performance Results

## Slide 12
Optimized Component Weights | Optimized Component Weights
Rotor Mass each | 7.8 grams
Motor Mass each | 13.2 grams
Esc mass each | 1.321 grams
Battery Mass | 236.4 grams
Airframe Mass | 272 grams
Payload Mass | 200 grams
Total GTOW | 730 grams
Weight Estimation

## Slide 13
Control Aspects of a Tricopter

## Slide 14
Physical Modelling
  NED Coordinate system has been implemented
  Assumption : Thrust forces and rotational moments generated by individual motors are proportional to the square of the motor speed values
  Servo is used on the tail to balance the gyroscopic moments generated by the motor movements during operations.
  Without servo the tricopter will rotate minimally around its axis while hovering
  To balance all these the 2 remaining motors must rotate in opposite direction , shift the center of mass closer to the front of the tricopter such that large angle of deflection to the tail motor has been reduced
Source : Salwa, M. ,Izabela Krzysztofik. “Optimal Control for a Three-Rotor Unmanned Aerial Vehicle in Programmed Flights”. Applied Sciences, 13(24), 13118. https://doi.org/10.3390/app132413118
Source : Ardupilot.org

## Slide 15
  kt = Thrust coefficient
  kd = Torque coefficient
  alpha ( ) = angle of inclination of the tail motor
  Uz = Thrust force
  U = Rotation force around the x-axis
  U = Rotation force around the y-axis
  U =Rotation force around the z-axis
  U = Force resulting from inclination of tail motor
  = Motor Speed
Physical Modelling
Source : Salwa, M. ,Izabela Krzysztofik. “Optimal Control for a Three-Rotor Unmanned Aerial Vehicle in Programmed Flights”. Applied Sciences, 13(24), 13118. https://doi.org/10.3390/app132413118

## Slide 16
Yaw control
Tail Rotor
Physical Modelling
Altitude control
Roll Control
Pitch control

## Slide 17
Mathematical Modelling
Equations of Motion (Non Linear)
Linearised Translational EOM
Linearised Rotational EOM

## Slide 18
Xd , Yd
Control Allocation
6 DOF Tricopter Dynamics
X-position
y-position
x-velocity
y-velocity
Roll
Pitch
Yaw
Roll rate
Pitch rate
Yaw rate
Attitude Control
Thrust (Fz)
Zd
1
2
3
Control System Architecture
Z
Vxd
[p q r]`
d
[ , , ]`
[Vx , Vy , ]`
[x , y , ]`
Vyd
d
d
p
d
d
q
d
r
d
T
x
T
y
T
z
Source :

## Slide 19
Control Design in Simulink

## Slide 20
Animation & Results
Circular Trajectory

## Slide 21
Animation & Results
Spiral Trajectory

## Slide 22
Animation & Results
Figure 8 Maneuver

## Slide 23
Structural Analysis of Tricopter
Hand Calculation
P
L
L : Arm Length
P : Force acting on the beam
Using equilibrium equation to calculation deflection of a cantilever beam
Given :
P = 8 N , length = 250 mm , diameter = 16 mm
Formula used :
Deflection : δ=PL³ / (3*E*I)
Moment of Inertia : I=πD⁴/(64)
Bending Stress : σ=M*R​/I
Results :
Moment of Inertia (I): 3.2170e-09 m^4
Maximum Deflection at Free End: 0.1772 mm
Maximum Bending Moment at Fixed End: 2.00 N·m

## Slide 24
Geometry Creation , Boundary Conditions & Meshing
Structural Analysis of Tricopter
Creation of solid body in solidworks/spaceclaim
Assigning of Material Properties
Boundary Condition : Fixed Support at the bottom
Boundary Condition : Force acting at the placed motor of 10 N
Meshed Part

## Slide 25
Mesh Parameter | Value
Nodes | 388996
Elements | 94485
Orthogonal Quality | Min : 0.054 Max : 0.999 Average : 0.813
Jacobian Ratio | Min : 1 Max : 12.25 Average : 1.77
Aspect Ratio | Min : 1.001 Max : 15.12 Average : 2.47
Mesh Criteria

## Slide 26
Static Structural Results
Total Deformation
Von Mises Stress
Von Mises Strain

## Slide 27
Modal Analysis
First 10 mode frequency for the same boundary condition of fixed support
Bending Mode at frequency 411.7 Hz
Torsional Mode at frequency 438.11 Hz
These are the natural frequency of the given body and the boundary conditions , since its a whole solid body the natural frequency tend to increase .

## Slide 28
Conclusion
  A preliminary design involving the performance , control and structural aspects of tricopter was introduced.
  Different trajectories and response was shown in the control design of the tricopter which would be required since the application involved is such.
  Basic structural aspect from hand calculation to the FEM analysis was shown and how it affects the result was discussed.

## Slide 29
Things that can be improved
  Structural Analysis of a hollow components of tricopter
  Ground effect and Wind model addition in the controller design
  Performance code validation through CFD
  Addition of filters to the control design to depict more accurate response .

## Slide 30
Softwares/Tools used
  Solidworks - (CAD Design)
  OpenVSP - Initial Sketch Configuration
  ANSYS - Static Structural & Modal Analysis
  MATLAB , Simulink - Flight Controls
  XFLR5 for airfoil analysis

## Slide 31
THANK YOU